DOS WIZARD

   Copyright 1983 by Gary C. Crider

INTRODUCTION

     DOS WIZARD was written to
accomplish several tasks that no
other disk utility seemed to address.
Some of these are listed below.  Some
knowledge of DOS file structures is
assumed. There are many good
tutorials on DOS available (see
BIBLIOGRAPHY).  IT IS IMPORTANT THAT
YOU UNDERSTAND WHAT YOU ARE DOING
WHEN YOU USE DOS WIZARD.  It will be
one of your handiest utilities, but
also one of the most potentially
dangerous if you don't understand it.
PLEASE READ THIS DOCUMENTATION
THOROUGHLY!
   1. RECOVERING THE SECTORS THAT
JUST SEEM TO VANISH FROM DOS DISKS.
When a directory listing is produced,
the sum of all file sectors plus the
remaining free sectors should total
707.  You have probably noticed that
this is not always true.  The primary
cause for this is pressing SYSTEM
RESET while a file is open for
output.  This leaves the directory
entry marked open and the file and
its associated sectors are forever
lost to DOS.
      Prior to DOS WIZ the only way
to reclaim the sectors was to copy
all good files to another disk,
reformat the bad disk and selectively
copy each good file back to the
reformatted diskette.
      DOS WIZ will read all files
while noting the sectors used by the
files. Any sector not referenced by a
file entry will be freed into the
available sectors pool and all open
file directory entries will be
released for reuse.  
     2. You probably have received
the notorious ERROR 164 or ERROR 144
at one time or another when trying to
read a disk file. Sometimes you can't
even delete a file because DOS wants
a valid file chain before he will
delete.





     All sectors used by a DOS file
are chained together, that is, a
sector of data has a pointer to the
next sector belonging to that file.
Also on each sector is a reference to
the file which owns it. ERROR 164
indicates that a sector was pointed
to by a prior sector, but the two
sectors do not reference the same
file.  This means that somehow
another file used a sector belonging
to the file in question.  ERROR 144
generally indicates that a sector has
for some reason become unreadable.
This can also be the indicated by
some other error codes.
      In either case, the integrity
of the file chain is lost and DOS
will not be able to read the file.
Usually there is nothing that can be
done because a binary load file or a
tokenized BASIC file that is not
complete will not be usable in any
fashion.  However, recovering a
portion of a data file can be very
useful at times. It can prevent a lot
of re-entry of data.  DOS WIZ allows
recovery of any file up to the point
where the chain is broken.  This then
becomes a valid DOS file and can once
again be accessed.
     3.  A bad sector on a disk is
often a big headache even when your
file is backed up.  It means that all
good files must be copied and the
disk reformatted and the good files
copied back. Only then can you
restore your file from the backup.
     DOS WIZ allows another approach
that is very often successful.  You
can analyze the disk to get the
location of the bad sector and it's
associated file name.  You can then
write zeros to that sector and the
odds are very good that you will then
be able to read it again. If you
can't you haven't lost anything since
the sector was unreadable.  You may
then recover the file up to the point
of the zero sector and then delete
the file. Now you can recover the
sectors used by the file and then
rewrite your backup file to the disk.
It sounds complicated, but is really
quite simple and much easier than the
alternative discussed earlier.





     4. Occasionally a file gets
deleted by mistake.  If the sectors
used by that file have not been
overwritten, DOS WIZ will allow easy
recovery of the file.
     5. Sometimes you end up with two
or more files of the same name.  If
you delete or rename one with DOS,
all files with that name are deleted
or renamed. DOS WIZ lets you delete
or rename by file number.  There are
never duplicate file numbers.
     6. DOS WIZARD provides a
translation of the sector bit map
from the VTOC that is easily
readable.  It allows you to "hide"
sectors from use by DOS by marking
them as allocated.  You can also free
allocated sectors.
     7. DOS WIZARD's directory
listing lists ALL entries including
deleted and open files.  It allows
you to perform many DOS functions on
those files by simply referencing the
file number.  This does however
eliminate the use of wild cards.  The
directory listing also tells you at a
glance whether any sectors are
unaccounted for.
     8. DOS WIZARD will allow you to
flag sectors as allocated and
effectively hide them from DOS so
that they will be reserved for your
use.
     9. DOS WIZARD can be used to
clear unused sectors of data. This
will speed up the disk duplication
process when FASTDUP (Copyright 1982
by Gary C. Crider) is used.
    10. DOS WIZARD will display
sectors in hex and ASCII on the same
screen. It also gives much valuable
information about that sector such as
the file to which it belongs.
    11. DOS WIZARD will list all
extents by sector range which are
occupied by a given file.  An extent
is a set of contiguous sectors.





PRINTING THE DOSWIZ DOCUMENTATION

     Running the DOSWIZ.PRT program
using BASIC will print the
DOSWIZ.DOC file in 1.75 width letters
on a STAR (tm) GEMINI series printer.
It may work on other printers as
well.
     Another way to print it would be
to use the COPY feature of your DOS
or DUP.SYS utility, specifying P: as
the output file name.  It can also be
printed from most word processors.
The actual GEMINI control characters
for page skipping are imbedded in the
text.  If you have a different brand
of printer, you may want to change
them.  They should work okay on the
EPSON (tm) printers.





 A  DISKETTE ANALYSIS

     This MENU option performs a
two-stage analysis of the contents of
a DOS format diskette. Either stage
may be interrupted by pressing the
ESC key, but any statistics will only
be valid up to the point where the
interrupt occurred.
     Stage 1 reads all DOS files
which are not marked as deleted or
open and verifies that the chain is
intact. All chain errors are reported
with the sector number where the
violation occurred and the file name
for the chain being validated. A
chain error is reported if:
     a) The file number in the sector
does not reflect the file being
validated;
     b) The next sector pointer does
not point to a valid sector number;
     c) The sector is not marked as
allocated in the VTOC;
     d) A read error occurs while
trying to read the sector;
     e) The byte count in the sector
is less than 1 or greater than 125.
     Stage 1 reports the following
counts:
     1. VALID FILES - the number of
files which are accessible by DOS and
contain no chain errors.
     2. DELETED FILES - the number of
directory entries flagged as deleted.
     3. OPEN FILES - the number of
directory entries flagged as open.
     4. BAD CHAINS - the number of
files which were found to have
invalid chains.
     5. SECTORS ALLOCATED - the
number of sectors which are marked as
allocated in the Volume Table Of
Contents (VTOC).
     6. FREE SECTORS - the number of
sectors marked as not allocated in
the VTOC.
     7. DEAD SECTORS - the number of
sectors allocated less the number of
sectors validated while verifying
chains.  These sectors cannot be
referenced by DOS.
     Stage 2 reads every sector on
the diskette and reports the count of
sectors containing no data (ZERO
SECTORS) and the count of sectors
which could not be read (BAD
SECTORS).





     Stage 2 will list by sector
number the first 64 bad sectors
encountered.  If there are more than
64 and you need to know where they
are, consider using FASTDUP.

 C  CHANGE DISKETTES

     This function must be performed
before processing a different
diskette since the VTOC and directory
are read into core only once by DOS
WIZARD.

 D  DISPLAY DIRECTORY

     This MENU function lists all
directory entries currently in use or
formerly used on this diskette.  It
also gives access to many functions
which may be performed on a file.
     The directory listing provides
the following for each file:
     a) FILE#- This is the number of
the directory entry.  They are
numbered from 0-63;
     b) NAME- This is the file name
contained in this directory entry
  Files which are recognizable and
accessible by DOS are in REVERSE
VIDEO.  These would appear in a DOS
directory listing;
     c) START- The starting sector
number for this file;
     d) COUNT- The number of
sectors used by this file;
     e) STATUS- Will contain "D" if
the file has been marked deleted, "O"
if it is marked as open, and "L" if
the file is locked.
     The display trailer contains the
number of free sectors and the number
of sectors accounted for which should
equal 707. If this number is other
than 707, there are dead sectors on
the disk. However there could still
be dead sectors even if there are 707
sectors accounted for. DISKETTE
ANALYSIS can be used to reveal this
condition.
     DISPLAY DIRECTORY allows the
following functions to be performed:
     a) UNLOCK - unlock file by
specifying file number.
     b) LOCK - lock file by
specifying file number.





     c) DELETE - delete file by file
number.  This will delete the entry
and free all sectors up to
encountering any chain error.  This
can be used when DOS delete will not
work due to errors.  If a file will
not delete with DOS WIZ, do a RECOVER
FILE (R) against the file and then
delete it.
     d) RENAME - rename a file by
specifying a name for a file number.
     e) LIST FILE EXTENTS - obtain a
list of all areas of contiguous
sectors occupied by a file.
     f) RECOVER FILE - recover a
deleted file or a portion of a file
with a broken chain.  If the file is
an open file, an extender will be
used of Xnn where nn is the file
number. This prevents duplicate file
names due to having recreated a file
that was open and thought to be lost.
File recovery makes a valid file out
of the portion of the file that can
be read up to the point of an error
being encountered, thus to DOS it is
now a good file but it may still be
useless to you.  You can salvage
portions of a data (LIST format) file
but BINARY LOAD AND CSAVEd FILES
CANNOT BE USED AFTER RECOVERY except
by the DELETE function of DOS WIZ or
DOS.

 M  SECTOR MAP

     This MENU function displays a
translation of the sector bit map
from the VTOC.  Each sector from
0-719 is represented by either a
period (free sector) or an asterisk
(allocated sector). Since sector 0
does not exist, it is always shown as
allocated.  Sector 720 is not
recognized by DOS and is not shown on
the map.
     To obtain the sector number of a
position on the map, add the numbers
from the scales on the left and top
of the screen.
     There are three functions
available from this screen:
     a) ALLOCATE SECTOR(S) - specify
starting and ending sector numbers
(inclusive).  These sectors will be
marked as allocated and will be
unavailable to DOS.  If the ending
sector is not specified, it will
default to the starting sector so
only one sector will be allocated.





     b) FREE SECTOR(S) - same as
above except sectors are marked as
free.  These sectors become available
for use by DOS when new sectors are
needed.
     c) RECLAIM LOST SECTORS - This
is the powerful recovery utility
discussed in the INTRODUCTION.  It
chases all non-deleted and unopened
file chains and remembers the good
sectors. Any sectors that are
allocated but not on a valid chain
are zeroed and released for use by
DOS.  If a chain error is
encountered, a message is displayed
indicating the sector and file. A
file recovery should be done on that
file (see DISPLAY DIRECTORY) and then
redo the reclaim function.  It is not
always necessary, but can't hurt
anything.

 S  DISPLAY SECTOR(S)

     This MENU function is used to
read a given sector and display it.
The left portion of the screen
displays hex representation of the
sector data while the right portion
displays most of the pertinent ASCII
characters represented by the sector
data.  The bottom of the screen has
valuable information about the
sector.  Information is displayed
only when pertinent to the sector
being displayed.
     a) SECTOR: This is the sector
number of the sector being displayed.
     b) NEXT SECTOR: This is the next
sector on the chain.  It is only
displayed when it is determined that
the current sector is indeed on a
chain.
     c) BYTES: This is the number of
bytes used by DOS in this sector.
     d) The lower left corner is used
to display the file name to which
this sector belongs and whether that
file is open, closed, deleted, or
locked.





     There are several options
available from this screen.  If you
press Z, 128 binary zeros will be
written in the sector.  If the sector
is allocated, it can be freed by
pressing F.  If it is free, it can be
allocated by pressing A.  Pressing L
will read the next sector on the
chain, while RETURN will read the
next sequential sector.
     If the sector is the last sector
on a chain then message END OF CHAIN
will appear in the trailer in place
of NEXT SECTOR.

 Z  ZERO UNUSED SECTORS.

     This MENU function writes a
sector of binary zeros to all sectors
which are marked free in the VTOC.
This is beneficial if you use my
FASTDUP program to duplicate disks.
Since FASTDUP does not store or write
any sectors which contain all zeros,
getting rid of unused data can speed
up the duplication process.  The
delete functions of DUP.SYS and DOS
WIZARD do not zero sectors as they
delete the file.  This is good since
mistakenly deleted files can
sometimes be recovered with DOS WIZ.  
CAUTION--If you have sectors marked
as allocated but they are not on a
file chain (to protect them from use
by DOS), this function will not zero
those sectors, but the RECLAIM
function of the SECTOR MAP will.
Know what you are doing!





GENERAL INFORMATION

     DOS WIZARD will work in a 24K+
ATARI 400 or 800 (ROM A or B).  It is
doubtful that it will work on the new
XL machines.  DO NOT USE ON DOUBLE
DENSITY disks or OS/A+ Version 4
files.  It will work on the ATARI 810
DOS Version 2 files and OS/A+ Version
2 files.  All 810 compatable drives
should work fine with DOS WIZARD.

     This program has undergone
extensive testing, but the
flexibility and versatility of the
program makes complete testing
difficult.  Please contact me at the
address/phone number below if you
discover errors.  Please have good
documentation of the problem so that
it can be recreated.  Also please
contact me with ideas for future
enhancements.
     DOS WIZARD was written for my
own use and for my friends in the
North Texas Atari Computer Team of
Fort Worth, Texas.  Please do not
sell this product for profit.  Make
as many copies as you like, but GIVE
them to your friends.
     Send all correspondence to:

GARY C. CRIDER
1105 BURGESS COURT
ARLINGTON, TEXAS 76015
(817) 467-1114






BIBLIOGRAPHY

     The following publications
(among others) have good explanations
of DOS file formats and disk struc-
tures:

DE RE ATARI by Chris Crawford, et al.

INSIDE ATARI DOS by Bill Wilkinson of
Optimized Systems Software, Inc..
Published by COMPUTE! Books of
Greensboro, North Carolina.


If all this went by faster than you
could read it, list it again and use
CTRL-1 to stop the display wherever
you want and then CTRL-1 again will
resume listing.


OTHER PRODUCTS BY GARY CRIDER:

FASTDUP- Sector-by sector disk
     duplicator.
DISASSEMBLER 6502- Reassembleable
     disassemblies from disk boot
     files, binary load files,
     selected sectors or memory to
     disk, printer and/or screen.
THE SHADOW- You have to see it to
     appreciate it.  Full buffer
     copying of multiple files.
     Crosses densities even on a
     single drive system.  Many nice
     and convenient features.  You
     may never use DOS copy again.