## Slide 1: Review: Simultaneous Internal Diffusion & External Diffusion
CAb
CAs
C(r)
At steady-state: transport of reactants from bulk fluid to external catalyst surface is equal to net rate of reactant consumption in/on the pellet
Molar rate of mass transfer from bulk fluid to external surface:
molar flux
external surface area per unit reactor volume
reactor volume
This molar rate of mass transfer to surface is equal to net rxn rate on & in pellet!
Goal: Derive a new rate eq that accounts for internal & external diffusion
-r’A is a function of reactant concentration
Reactant conc is affected by internal & external diffusion
Express reactant conc in terms of diffusion-related constants & variables
→Use mole balance
Extn
diff
Intern
diff

## Slide 2: Review: Basic Molar Balance at Spherical Pellet Surface
=
Flux: bulk to external surface
Actual rxn rate per unit total S.A.
External S.A.
x
ac: external surface area per reactor volume (m2/m3)
DV: reactor volume (m3) f: porosity of bed (void fraction)
-r’’A: rate of reaction per unit surface area (mol/m2·s)
-r’A: mol/g cat∙s -rA: mol/volume∙s
Sa: surface area of catalyst per unit mass of catalyst (m2/g cat)
rb: bulk density, catalyst mass/ reactor volume rb=rc(1-f)
x
external + internal S.A.
For a 1st order reaction, simplifies to:
per mass cat→
per surface area
per volume

## Slide 3: Review: Effectiveness Factors
Remember, the internal effectiveness factor is based on CAs
The overall effectiveness factor is based on CAb:
Put into design eq to account for internal & external diffusion
Omega

## Slide 4: Review: Reaction Rate Variation vs Reactor Conditions
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
External diffusion
Surface reaction -r’A=kCA
Internal diffusion

## Slide 5: L22: Nonideal Flow & Reactor Design
So far, the reactors we have considered ideal flow patterns
  Residence time of all molecules are identical
  Perfectly mixed CSTRs & batch reactors
  No radial diffusion in a PFR/PBR
    Goal: mathematically describe non-ideal flow and solve design problems for reactors with nonideal flow
      Identify possible deviations
      Measurement of residence time distribution
      Models for mixing
      Calculation of exit conversion in real reactors

## Slide 6: Nonideal Flow in a CSTR
Dead Zone
Ideal CSTR: uniform reactant concentration throughout the vessel
Real stirred tank
  Relatively high reactant concentration at the feed entrance
  Relatively low concentration in the stagnant regions, called dead zones (usually corners and behind baffles)
Short Circuiting
Dead Zone

## Slide 7: Nonideal Flow in a PBR
Ideal plug flow reactor: all reactant and product molecules at any given axial position move at same rate in the direction of the bulk fluid flow
Real plug flow reactor: fluid velocity profiles, turbulent mixing, & molecular diffusion cause molecules to move with changing speeds and in different directions
channeling
Dead zones

## Slide 8: Residence Time Distribution (RTD)
Measurement of RTD
RTD is measured experimentally by injecting an inert “tracer” at t=0 and measuring the tracer concentration C(t) at the exit as a function of time
Tracer should be easy to detect & have physical properties similar to the reactant
Flow through a reactor is characterized by:
The amount of time molecules spend in the reactor, called the RTD
Quality of mixing
RTD ≡ E(t) ≡ “residence time distribution” function
Pulse injection
Detection
(PBR or PFR)
This plot would have the same shape as the pulse injection if the reactor had perfect plug flow

## Slide 9
t
Tracer Conc

t
Tracer Conc
t
Tracer Conc

Nearly ideal PFR
Nearly ideal CSTR
PBR w/ channeling & dead zones
t
Tracer Conc
CSTR with dead zones
RTD Profiles & Cum RTD Function F(t)

## Slide 10: Calculation of RTD
RTD ≡ E(t) ≡ “residence time distribution” function
RTD describes the amount of time molecules have spent in the reactor
C(t)
The C curve
t
Fraction of material leaving the reactor that has resided in the reactor for a time between t1 & t2
E(t)=0 for t<0 since no fluid can exit before it enters
E(t)≥0 for t>0 since mass fractions are always positive
Fraction of fluid element in the exit stream with age less than t1 is:

## Slide 11
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
Chart: t (min)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
Plot C vs time:
Tabulate E(t): divide C(t) by the total area under the C(t) curve, which must be numerically evaluated

## Slide 12
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
Chart: t (min)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
Plot C vs time:
Tabulate E(t): divide C(t) by the total area under the C(t) curve, which must be numerically evaluated

## Slide 13
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
Tabulate E(t): divide C(t) by the total area under the C(t) curve:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Plot E vs time:
Chart: t (min)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
 | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0

## Slide 14
E vs time:
Chart: t (min)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
 | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Fraction of material that spent between 3 & 6 min in reactor = area under E(t) curve between 3 & 6 min
Evaluate numerically:

## Slide 15: Step-Input to Determine E(t)
Disadvantages of pulse input:
Injection must be done in a very short time
Can be inaccurate when the c-curve has a long tail
Amount of tracer used must be known
Alternatively, E(t) can be determined using a step input:
Conc. of tracer is kept constant until outlet conc. = inlet conc.
injection
detection
The C curve
t
Cin
t
t
Cout
t
C0
C0

## Slide 16
Questions
1. Which of the following graphs would you expect to see if a pulse tracer test were performed on an ideal CSTR?
t
Tracer Conc
t
Tracer Conc
t
Tracer Conc

t
Tracer Conc
A
B
C
D
2. Which of the following graphs would you expect to see if a pulse tracer test were performed on a PBR that had dead zones?
t
Tracer Conc
t
Tracer Conc
t
Tracer Conc

t
Tracer Conc
A
B
C
D

## Slide 17: Cumulative RTD Function F(t)
F(t) = fraction of effluent that has been in the reactor for less than time t
t
F(t)
80% of the molecules spend 40 min or less in the reactor
40
0.8

## Slide 18: Relationship between E & F Curves
F(t) = fraction of effluent that has been in the reactor for less than time t
E(t)= Fraction of material leaving reactor that was inside for a time between t1 & t2

## Slide 19
t
C(t)

t
C(t)
t
C(t)

Nearly ideal PFR
Nearly ideal CSTR
PBR with channeling & dead zones
t
C(t)
CSTR with dead zones
40
t (min)
F(t)
0.8
80% of the molecules spend 40 min or less in the reactor
F(t)=fraction of effluent in the reactor less for than time t
Boundary Conditions for the
Cum RTD Function F(t)

## Slide 20: Mean Residence Time, tm
For an ideal reactor, the space time  is defined as V/u0
The mean residence time tm is equal to  in either ideal or nonideal reactors
By calculating tm, the reactor V can be determined from a tracer experiment
The spread of the distribution (variance):
Space time t and mean residence time tm would be equal if the following two conditions are satisfied:
  No density change
  No backmixing
In practical reactors the above two may not be valid, hence there will be a difference between them

## Slide 21: RTD in Ideal Reactors
All the molecules leaving a PFR have spent ~ the same amount of time in the PFR, so the residence time distribution function is:
The Dirac delta function satisfies:
Zero everywhere but one point
…but =1 over the entire interval