## Slide 1: Review: Equilibrium Conversion XAe
T
XA,e
0
1
exothermic
endothermic
Example) A⇌B CA0=1 CB0=0
Rearrange to solve in terms of XAe
This equation enables us to express Xae as a function of T

## Slide 2: Review: XAe and Temperature
Makes sense from Le Chatelier’s principle
Exothermic rxn produces heat→
increasing temp adds heat (product) & pushes rxn to left (lower conversion)
Makes sense from Le Chatelier’s principle
Heat is a reactant in an endothermic rxn→
increasing temp adds reactant (heat) & pushes rxn to right (higher conversion)
Clicker question material

## Slide 3: Review: Optimum Feed Temperature
For reversible, exothermic rxns, optimize feed temperature to maximize XA
From thermodynamics
XEB
T
600
500
350
0.15
0.33
0.75
XA
W
T0 = 600
T0 = 500
T0 = 350
High T0: moves XA,EB line to the right. Rxn reaches equilibrium fast, but low XA
Low T0 would give high XA,e but the specific reaction rate k is so small that most of the reactant passes through the reactor without reacting (never reach XA,e)

## Slide 4: Review: Interstage Cooling
XEB
T
final conversion
XA,EB1
cooling process
XA,EB2
XA,EB3
XA,EB4
T0
Reactor 4
Reactor 1
Cooling, C1
C2
C3
Reactor 3
Reactor 2
Each reactor operates adiabatically
Adiabatic operation of each reactor simplifies the energy balance
Higher feed temp- reaction reaches equilibrium quickly but XA,e is low
Lower feed temp- higher XA,e but reaction rate is too slow to be practical
Cooling between reactors shifts XA,EB line to the left, increasing XA

## Slide 5: Review: Endothermic Reactions
The equilibrium conversion increases with increasing temperature, so use interstage heating to increase the conversion
XEB
T
heating process
final conversion
Red lines are from the energy balance, slant backwards because DH°RX >0 for endothermic reaction

## Slide 6: L14: Nonadiabatic PFR/PBR Operation and Reactor Stability
T changes with distance down reactor- differential form of EB must be used
Multiple steady states: more than one set of conditions satisfies both the energy balance & mole balance

## Slide 7: Review: Application to a SS PFR
PFR
FA0
FA
distance
T
XA
Negligible shaft work (ẆS=0) and adiabatic (Q=0)
Use TEB to construct a table of T as a function of XA
Use k = Ae-E/RT to obtain k as a function of XA
Use stoichiometry to obtain –rA as a function of XA
Calculate:
may use numerical methods

## Slide 8: Steady-State PFR/PBR w/ Heat Exchanger
Heat is added or removed through the cylindrical walls of the reactor
FA0
T0
FAe
Te
Ta
T
V
V+V
Energy balance on small volume of SS PFR:
0
Heat exchange area per volume of reactor
Take limit as DV→∞:
Expand:
Plug in Q:

## Slide 9: TEB for PFR/PBR w/ Heat Exchanger
FA0
T0
FAe
Te
Ta
T
V
V+V
Substitute the differentials:
Solve for dT/dV:

## Slide 10: Energy Balance for Tubular Reactors
Heat generated
Heat removed
Heat generated
Heat removed
Substitute and multiply out the denominator
Energy balance for SS PFR, Ẇs=0
PFR energy balance is coupled to the PFR design eq, and PFR design eq is coupled to Arrhenius eq for k or Kequil
(these are the 3 equations that must be simultaneously solved)
Multiply Ua and (Ta-T) by
-1 (-1 x -1 = 1)
Switched sign & order in bracket

## Slide 11: Liquid Phase Reaction in PFR
Mole balance
Rate law
Stoichiometry
Combine
with
Energy balance
Solve these equations simultaneously with an ODE solver (Polymath)
If this were a gas phase rxn w/ pressure drop, change stoichiometry accordingly & include an equation for dDP/dW

## Slide 12: Review: Nonisothermal CSTR
Solve TEB for T at the exit (Texit = Tinside reactor)
Calculate k = Ae-E/RT where T was calculated in step a
Plug the k calculated in step b into the design equation to calculate VCSTR
Case 1: Given FA0, CA0, A, E, Cpi, H°I, and XA, calculate T & V
Solve TEB for T as a function of XA
Solve CSTR design equation for XA as a function of T (plug in k = Ae-E/RT )
Plot XA,EB vs T & XA,MB vs T on the same graph. The intersection of these 2 lines is the conditions (T and XA) that satisfies the energy & mass balance
Case 2: Given FA0, CA0, A, E, Cpi, H°I, and V, calculate T & XA
XA,EB = conversion determined from the TEB equation
XA,MB = conversion determined using the design equation
XA
T
XA,EB
XA,MB
XA,exit
Texit
Intersection is T and XA that satisfies both equations
Isothermal CSTR: feed temp = temperature inside the CSTR

## Slide 13: Multiple Steady States in CSTR
Chart: T (K)
| 50 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
EB conversion | -1.235 | -0.91 | -0.7475 | -0.585 | -0.4225 | -0.26 | -0.0975 | 0.065 | 0.2275 | 0.377 | 0.5525 | 0.715 | 0.8775 | 1.04 | 1.2025 | 1.365 | 1.69 | 2.015 | 2.34
Equilibrium conversion | 5.9222e-30 | 1.5069e-12 | 4.5627e-09 | 9.5492e-07 | 4.3414e-05 | 0.00075958 | 0.0069957 | 0.040148 | 0.15228 | 0.35618 | 0.62839 | 0.80316 | 0.89748 | 0.94467 | 0.96853 | 0.98112 | 0.99217 | 0.9962 | 0.99793
Plot of XA,EB vs T and XA,MB vs T
Intersections are the T and XA that satisfy both the mass balance and energy balance
Multiple sets of conditions are possible for the same rxn in the same reactor with the same inlet conditions!
Reactor must operate near one of these steady states- this requires knowledge of their stability!
XA,MB

## Slide 14
Consider a jacketed CSTR with constant heat capacity, negligible shaft work, DCP=0, first order kinetics, all feeds at the same temperature (Ti0=T0), constant Ta in jacket, and an overall heat transfer coefficient
Substituting for
Heat removed term ≡ R(T)
Heat generated term ≡ G(T)
A steady-state occurs when R(T) = G(T)
Bring terms that remove heat to other side of equation:

## Slide 15: Even More Terms…
Heat removed term ≡ R(T)
Heat generated term ≡ G(T)
Substitute
More substitutions:
Heat removed:
Heat generated:

## Slide 16: Heat Removal Term and T0
T
R(T)
Increase T0
T
R(T)
Increase 
T0
Ta
 = 0
 = ∞
For Ta < T0
Heat removed: R(T)
Heat generated G(T)
When T0 increases, slope stays same & line shifts to right
R(T) line has slope of CP0(1+k)
When k increases from lowering FA0 or increasing heat exchange, slope and x-intercept moves
Ta<T0: x-intercept shifts left as k↑
Ta>T0: x-intercept shifts right as k↑
k=0, then TC=T0
k=∞, then TC=Ta
Notes: Think share pair: after “When T0 increases, slope stays same & line shifts to right” appears, ask them to discuss with neighbor why the slope doesn’t change. Answer: slope = Cpo(1+kappa) and initial temp (To) is not in expression for kappa, so it does not affect slope.
Think share pair: why does changing kappa affect the slope and intercept? Answer: kappa is a variable in both the slope and intercept portion of line.

## Slide 17: CSTR Stability
Chart: T
1
2
3
3 steady states satisfy the TEB and BMB
Suppose a disturbance causes the reactor T to drift to a T between SS1 & SS2
R(T) > G(T) so T gradually falls to T=SS1
Suppose a disturbance causes the reactor T to drift to a T between SS2 & SS3
G(T) > R(T) so T gradually rises to T=SS3
Suppose a disturbance causes the reactor T to drop below SS1
G(T) > R(T) so T gradually rises to T=SS1
Suppose a disturbance causes the reactor T to rise above SS3
R(T) > G(T) so T gradually falls to T=SS3
SS1 and SS3 are locally stable (return to them after temp pulse)
SS2 is an unstable- do not return to SS2 if there is a temp pulse
Temperature
G(T) & R(T)

## Slide 18: Multiple Steady States and T0
TT
R(T), G(T)
T
T0,1
T0,2
T0,3
T0,4
T0,5
T0,6
Changing the inlet T will shift the steady state temperature (TS)
Notice that the number of steady state temperatures depends on T0
Increasing T above these TS cause a temperature jump to the higher TS

## Slide 19: Temperature Ignition-Extinction Curve
Unstable
steady states
Slight increase in T above TS,green causes reactor T to jump to TS,cyan
T0, entering temperature
Ts, steady-state temp
ignition temperature
extinction temperature
Upper steady state
Lower steady state
Plot TS vs T0
TS,upper
TS,lower
TS along dashed line are unstable
R(T), G(T)
T
Ignition temp: T where jump from TS,lower to TS,upper occurs
Slight decrease in T below TS,magenta causes reactor T to drop to TS,yellow
Extinction temp: T where drop from TS,upper to TS,lower occurs

## Slide 20: Runaway Reaction
Ignition temperature is very important: once T0 exceeds Tignition, transition to the upper steady state will occur
  undesirable
  dangerous
Runaway reaction
R(T) only intersects with upper steady state
R(T), G(T)
T